## Slide 1: IPv6 Tunnel Brokers
Matt Ryanczak
Network Operations Manager
How to Setup an IPv6 Tunnel Using a Public Tunnel Broker and Windows

## Slide 2: What is an IPv6 Tunnel?
IPv6 encapsulated in another protocol
  Usually IPv4 but other protocols work too
Common implementations
  6in4 (RFC3056)
  Protocol 41 (RFC2893 & RFC1933)
  Anything in Anything (AYIYA) (http://www.sixxs.net/tools/ayiya)
IPv6 in IPv4 Tunnel

## Slide 3: What is a Tunnel Broker?
A provider of IPv6 tunneling services
At least 12 public tunnel brokers
Use various provisioning techniques
  Static
  Dynamic (via helpers)
Some provide /48s, reverse DNS, BGP
Most are FREE

## Slide 4: List of Tunnel Brokers
Provider | Website | Region
Hurricane Electric | http://www.tunnelbroker.net | US (Global)
SixXS | http://www.sixxs.net | Europe (Global)
Go6 (Hexago) | http://www.go6.net | Canada (Global)
IIJ | http://www.iij.ad.jp/en/service/IPv6/index.html | Japan
IPv6Now | http://www.ipv6now.com.au/ | Australia
Renater | http://tunnel-broker.renater.fr/ | France

## Slide 5: Setting up a Tunnel with Go6

## Slide 6: Why Go6?
Easy to setup client for many Oses
Supports clients behind NATs
Provides /48 networks
Support forum

## Slide 7: 3 Easy Steps
Create Account
Download and Install Software
Run Software

## Slide 8: Create an Account

## Slide 9: Create an Account
Enter Your Information
Required Fields:
- Name
- Username
- E-mail
- Password
You are automatically signed in once you submit the form

## Slide 10: Download Go6 Client

## Slide 11: Install Go6 Client

## Slide 12: Run the Go6 Client
Works out of the box if:
- You have public IP address
- No Filters / Firewalls
Notice that:
- Configured for anonymous access
- Defaults to starting on boot

## Slide 13: Run the Go6 Client

## Slide 14: Run the Go6 Client
From command prompt:
- Tunnel adapter listed
- Valid global IPv6 address

## Slide 15: Troubleshooting
Enable verbose logging
Open log window
Visit Forums:
http://forum.go6.net/

## Slide 16: Troubleshooting
Advanced Tab
Tunnel Modes
  - NAT Traversal
Keep Alive Functionality
  - Increase Interval

## Slide 17: Now What?
http://www.arin.net
http://www.kame.net
http://www.sixxs.net/misc/coolstuff
http://ipv6.google.com
news://reader.ipv6.xsnews.nl
telnet://towel.blinkenlights.nl
telnet://mud.fataldimensions.org:4000

## Slide 18: Thank You!