## Slide 1: Hosting Providers and IPv6

## Slide 2
Managed Service Providers and Hosting Providers are an often overlooked player
  Neither a traditional ISP or a traditional Enterprise
  Toolsets are often too large and too broad or not scalable enough.
Use a vast array of equipment
  Switches
  Routers
  Load Balancers
  Firewalls
  IDS/IDP and other Security Products
  Servers
  Accessory Equipment
    PDU/KVM/Terminals
Often have standalone datacenters
  Often no nationwide/global Backbone
Hosting Providers

## Slide 3
Some ISP’s are giving away IPv6 Transit
Many ISP’s support Dual Stack if you ask
Existing Equipment Supports IPv6
  And has for some time
Its easy
No reason not to
IPv6 and the Hosting Provider

## Slide 4
What is right for you?
  You know your existing architecture
Dual Stack
  Simply add IPv6 addresses to existing equipment
Parallel
  Deploy discrete infrastructure
Hybrid
  Discrete for some (Like WAN Routers)
  Dual stack others (Core or Edge)
Introduce an IPv6 Architecture

## Slide 5
Servicing IPv6
  Process/Route IPv6 Traffic
Supporting IPv6
  Management functions
    SNMP, SYSLOG, SSH, NTP
Servicing IPv6 vs Supporting IPv6

## Slide 6
Routers
  Cisco and Juniper have supported IPv6 for ages
  Probably have something lying around
Switches
  Ethernet Layer2 doesn’t care
  Management may be IPv4 only
Load Balancers
  F5
    License on 1500 product line generation
    Standard on 1600 product line generation
  Citrix Netscaler
    Standard on 9.x
IPv6 Equipment

## Slide 7
Firewalls
  Cisco
    PIX/ASA 7.0+
  Juniper/Netscreen
    Screen OS 5.0+
Security Products
  Snort
  Juniper IDP
  Gigamon
Non Compliant Devices
  IPv6 to IPv4 Address Translations
IPv6 Equipment continued

## Slide 8
Monitoring
  Nagios
DNS
  Bind
Mail
  Sendmail
IPv6 Tools

## Slide 9
ISP vs End Users
IPv6 and Multiple Discrete Networks (MDN)
  NRPM 6.11
Hosting Providers and ARIN

## Slide 10
True IPv6 Only still difficult
  Management Services
  Router ID
Challenges